T.Moore
2.8.19
Notes taken from webpage: http://wiki.seeedstudio.com/GrovePi_Plus/
Git Base Hat Directory: https://github.com/raspberrypi/hats
GIT Project Directory: https://github.com/Seeed-Studio/grove.py

Setup Software on RPI for GrovePi Plus Board
2 ways to setup the board:
1. Using the BrickPi Image
  1. Download the Brick Pi Image and install the image on your SD card. Here is the link to the BrickPi Page with steps to configure the SD card. You will need a minimum of 4GB SD Card for this installation.
http://www.dexterindustries.com/BrickPi/getting-started/pi-prep/
  1. Clone the Github repository at an appropriate location in Raspbian
git clone https://github.com/DexterInd/GrovePi.git
  1. Run the bash script in the Scripts folder to configure the Raspbian. Here is the tutorial for setting up with the Script.
http://www.dexterindustries.com/GrovePi/get-started-with-the-grovepi/setting-software/
  1. Restart your Raspberry Pi.

1. Configure my own image using the OS of my choice
  1. Clone the Github repository at an appropriate location
git clone https://github.com/DexterInd/GrovePi.git
  1. Run the bash script in the Scripts folder to configure the Raspbian. here is the tutorial for setting up with the Script.
http://www.dexterindustries.com/GrovePi/get-started-with-the-grovepi/setting-software/
  1. Restart the Raspberry Pi and start using the Grove Pi.

RPI I2C Configuration
Step1: Use configuration tool “raspi-config”
Step2: Arrow down to ‘Interfacing Options’
Step3: Arrow down to P5 I2C and press "enter" to select. Then press yes. Then press OK.
Step4: Select ‘Finish’ to save the changes.

Usage
To use the grove modules, type..
$$ grove <TAB> to see the supported grove list of modules. For example:
pi@raspberrypi:~$ grove_
grove_3_axis_compass_bmm150 grove_i2c_color_sensor_v2 grove_mini_pir_motion_sensor grove_rotary_angle_sensor grove_temperature_sensor
grove_4_digit_display grove_i2c_motor_driver grove_moisture_sensor grove_ryb_led_button grove_thumb_joystick
grove_air_quality_sensor_v1_3 grove_lcd_1.2inches grove_oled_display_128x64 grove_servo grove_tilt_switch
grove_button grove_led grove_piezo_vibration_sensor grove_slide_potentiometer grove_touch_sensor
grove_collision_sensor grove_light_sensor_v1_2 grove_pwm_buzzer grove_sound_sensor grove_ultrasonic_ranger
grove_gesture_sensor grove_loudness_sensor grove_recorder_v3_0 grove_switch grove_water_sensor
grove_high_accuracy_temperature grove_mech_keycap grove_relay grove_temperature_humidity_sensor
pi@raspberrypi:~$ grove_

DIGITAL PORT Usage (Ultrasonic ranger):
$$ grove_ultrosonic_ranger 5 6
For most grove module, you need to add the pin number parameter, like:

$$ grove_ultrasonic_ranger 5 6
5 and 6 are the GPIO/BCM pin. However, you may have noticed that in the first example:
grove_pwm_buzzer
we didn't add a parameter after the command. This is because the PWM port and I2C port do not require pin number parameters. You can find the pin number silkscreen just besides the Grove socket.

ANALOG PORT USAGE (air quality sensor):
$$ grove_air_quality_sensor_v1_3 0 1
Make sure to use the pin # designations (0, 1) not the port # (A0, A1)

I2C PORT USAGE (OLED Display 128x64):
pi@raspberrypi:~$ grove_oled_display_128x64
pi@raspberrypi:~$

This will display the ‘hello world’ on the OLED.