T.Moore
2.7.19
Notes taken from webpage: http://wiki.seeedstudio.com/Grove-Temperature_and_Humidity_Sensor_Pro/
GIT Project Directory: https://github.com/Seeed-Studio/grove.py

Grove Temp & Humid Sensro Pro Library Setup
Temp sensor is connected to port 12 of the base hat.
Step1: Setting up software on RPI…

$$ curl -sL https://github.com/Seeed-Studio/grove.py/raw/master/install.sh | sudo bash -s -

Step2:
If everything goes well you should get:
Successfully installed grove.py-0.5
#######################################################
Lastest Grove.py from github install complete !!!!!
#######################################################

Step3:
Download the source file by cloning the grove.py library.
$$ cd ~
$$ git clone https://github.com/Seeed-Studio/grove.py
Usage
To use the grove modules, type..
$$ grove <TAB> to see the supported grove list of modules. For example:
pi@raspberrypi:~$ grove_
grove_3_axis_compass_bmm150 grove_i2c_color_sensor_v2 grove_mini_pir_motion_sensor grove_rotary_angle_sensor grove_temperature_sensor
grove_4_digit_display grove_i2c_motor_driver grove_moisture_sensor grove_ryb_led_button grove_thumb_joystick
grove_air_quality_sensor_v1_3 grove_lcd_1.2inches grove_oled_display_128x64 grove_servo grove_tilt_switch
grove_button grove_led grove_piezo_vibration_sensor grove_slide_potentiometer grove_touch_sensor
grove_collision_sensor grove_light_sensor_v1_2 grove_pwm_buzzer grove_sound_sensor grove_ultrasonic_ranger
grove_gesture_sensor grove_loudness_sensor grove_recorder_v3_0 grove_switch grove_water_sensor
grove_high_accuracy_temperature grove_mech_keycap grove_relay grove_temperature_humidity_sensor
pi@raspberrypi:~$ grove_

Temp & Humidity Sensor Pro Usage (With Grove Base Hat for Raspberry Pi) :
python grove_temperature_humidity_sensor.py <DHT Type> <pin #>
Example:
$$ cd grove.py/grove
$$ python grove_temperature_humidity_sensor.py 22 12
(DHT Type is 22, pin 12 is used)

Display Output:
pi@raspberrypi:~/grove.py/grove $ python grove_temperature_humidity_sensor.py 22 12
DHT22, humidity 49.2%, temperature 21.8*
DHT22, humidity 48.5%, temperature 21.9*
DHT22, humidity 48.1%, temperature 21.9*
DHT22, humidity 47.7%, temperature 22.0*
DHT22, humidity 47.1%, temperature 22.0*
DHT22, humidity 46.9%, temperature 22.0*
DHT22, humidity 49.3%, temperature 22.1*
DHT22, humidity 56.1%, temperature 22.2*